Report: Handyboard Communication Protocol
Wireless Mesh Network
Peter Fyon 100652096
peter.fyon@gmail.com
John Koh 100684909
johnnykoh.is@gmail.com
1.0 Introduction
The purpose of this paper is to define a standard protocol for communication between the controller handyboard and the car drive handyboard. The document will cover the functional requirements and technical implementation details.

2.0 Requirements
The following requirements were defined during the requirements elicitation process:
1. The controller will not send conflicting signals to the vehicle (Left and right, or forward and backwards).
2. The controller will be able to send both forward or backwards, and directional commands at the same time.
3. The controller will be able to centre the directional wheels.
4. If there is no command to send, the controller will send an opcode representing “do nothing”.
5. There will not be a significantly noticeable delay between when an input is supplied to the controller and when the corresponding action is taken by the vehicle.
6. The controller will send a packet approximately every 50 milliseconds.[1]
  [1] Through experimental testing, it was determined that an action taken by the vehicle every 50 ms (such as moving forward or backwards) was indistinguishable from continuous motion.
7. The vehicle will consume a packet approximately every 50 milliseconds.

3.0 Technical Specifications
The packet structure will be arranged as follows:
- Single byte packet containing opcode
  - Low five bits for forwards/backwards, left/right, and centre commands.
  - High 3 bits reserved for future use.

	Reserved	Reserved	Reserved	Centre	Forward	Backward	Left	Right
Centre Wheels:
	X	X	X	1	X	X	0	0
Do-Nothing
	X	X	X	0	0	0	0	0
Forward:
	X	X	X	X	1	0	X	X
Reverse:
	X	X	X	X	0	1	X	X
Left:
	X	X	X	0	X	X	1	0
Right:
	X	X	X	0	X	X	0	1

Note that while the controller may send multiple commands in the same packet, it is the responsibility of the controller to ensure that each command does not conflict with any others.

3.1 Encoding
Encoding is done on the controller. Every directional switch will add their corresponding instruction to the instruction packet. After collecting inputs, the controller will send the instruction packet to the R/C car.

3.2 Decoding
Decoding is done on the R/C car. The R/C car will decode the instructions by performing a bit-wise AND with the instruction packet and each possible instruction, except Do-Nothing. When a bit-wise AND returns true, the corresponding instruction will be performed. Once all the possible instructions are checked, the car will sleep.