Report: Handyboard Serial Port
Wireless Mesh Network
John Koh 100684909
johnnykoh.is@gmail.com
1.0 Introduction
The purpose of this paper is to report on our findings on the serial port and communication method used on the Handyboards. This report will cover the hardware functionality of the serial port on the Handyboard.

2.0 Analysis
In order to communicate with the Handyboard, the compiler must connect through the serial interface. By analyzing the hardware in between the serial interface and the Handyboard, the Handyboard can be configured to work with the XBee node.

3.0 Technical Specifications
See the attached diagram on the CPU and Memory Circuit Schematic.(page 37 in manual)

The Handyboard only has one pair of receive (RxD) and transmit (TxD) but uses an RJ14 plug, which normally houses two pairs. The following table is how the RJ14 plug is laid out on the Handyboard.

Position	RJ14 Pin	Pair	Tip/Ring	+/-	Colours (wire, Handyboard-side)
1
2	1	2	Tip	+	Black
3	2	1	Ring	-	Red
4	3	1	Tip	+	Green
5	4	2	Ring	-	Yellow
6