## Slide 1: ZigBee Mesh Network
SYSC 4907 Engineering Project

## Slide 2: Introduction
Group Members
Peter Fyon 100652096 CSE
John Koh 100684909 CSE
Andrew Kusz 100685317 CSE
Group Supervisors
Dr. Victor Aitken
Prof. Graham Eatherley

## Slide 3: Presentation Outline
Proposal
  Motivation and Objectives
Technical Overview
  Mesh Networking and ZigBee/IEEE 802.15.4
  Hardware
Progress
  Analysis and Design
  Implementation
Future Milestones
Future Projects

## Slide 4: Proposal
Motivation
Interest in a hardware and low-level software based project
Innovative and developing technology
Numerous real world applications

## Slide 5: Proposal
Objectives
To control a remote control (R/C) car over the ZigBee mesh network
  Seamlessly integrate hardware with the ZigBee mesh network
To prove any capable hardware can be integrated into a ZigBee mesh network
  Proof of concept
Provide an alternative to simple point-to-point wireless communication

## Slide 6: Technical Overview
Mesh Networking
Figure 1: Mesh Network

## Slide 7: Technical Overview
Figure 2: Mesh Network Self Healing

## Slide 8: Technical Overview
ZigBee and IEEE 802.15.4
IEEE 802.15.4 standard
  Defines physical and medium access control (MAC) layer
ZigBee: 802.15.4 specification
  Defines the network and application layer
  Supports self-healing mesh networking

## Slide 9: Technical Overview
XBee modules
Range: 40m indoors, 120m outdoors
Supply Voltage: 2.1V to 3.6V
Transmit Current: 45mA (in boost mode)
Transmission Rate: 250kbps
Figure 3: XBee module

## Slide 10: Technical Overview
Hardware
Handyboard
  Motorola 68HC11 @ 2 MHz system clock
    8 Bit MCU
  Four DC motor drivers
  UART
R/C cars

## Slide 11: Progress
Analysis and Design
XBee module to implement ZigBee – Why?
  Low cost
  User-friendly
  Low power consumption
  Large knowledge base
Notes: - Use of XBee modules over other chips
- Two development kits on hand (made us more familiar)
- Saves money
- Fairly user friendly
- Available in convenient PDIP (plastic dual inline package) compared to TI's smd (surface mount device) only chips
- Not too expensive (not doing large scale)
- Big community
- Low power modules:
- Easier to test the mesh network with, since we don't need large distances between the nodes
- More realistic for some applications
- Pin compatible with high-power (pro) nodes for extensibility
- cheaper

## Slide 12: Progress
Analysis and Design
Car
  Skid vs. Turn Steering
  Motor vs. Servo
Controller
  Control method
Notes: - Skid steering vs turn steering
- Turn steering is more precise
- Skid steering relies on friction between wheels and ground (which may not be the same across the car)
- Servo vs motor
- Motor = all left or all right
- Servo = fine control
- Not particularly useful for us, but for future designs we might want the fine control

## Slide 13: Progress
Analysis and Design
Handyboard
  Able to communicate with XBee nodes
  Readily available
  Familiar environment
  Powerful board
Notes: - Use of handyboards for cars and controller
- Many available in the lab
- If one board is defective, there are others we can use
- (saves money)
- Powerful enough to handle tasks (if a bit overpowered for the controller)
- No real drawback to using them over another board

## Slide 14: Progress
Analysis and Design
C vs. Interactive C vs. Assembly
  Complexity
  Reliability
  Cost
Notes: - C vs Interactive C vs Assembly
- Interactive had all the built in libraries
- Downside: poor community/documentation, not terribly efficient, not real-time
- Upside: Interactive C IDE is free
- C would need to write our own libraries
- Downside: more work, ICC11 is not free
- Upside: more control over board function, interrupts are easy to implement, can be real-time
- Assembly required for interrupts
- Downside: have to write our own libraries, we have less experience with asm, potentially less efficient than C with a good assembler
- Upside: can be more efficient code, control over all interrupts and board functions, can be real-time
- XBee modules are not real-time, but we need interrupts.
- Asm can be used (in theory) with interactive C to provide interrupts with the use of interactive C's libraries
- (even code given in the manual doesn't work reliably for interrupts)

## Slide 15: Progress
Figure 4: System Diagram

## Slide 16: Progress
Implementation
Communication protocol
Controller logic
Car driving logic
Notes: - Design of protocol
- Uses one byte for commands
- Four bits for motion
- Remaining four bits available for future designs
- Packet size is less than the maximum buffer size for XBees with security enabled (80 bytes), so payload can be sent in entirety in one frame
- Reduces overhead (in the form of headers for each packet) and network congestion by sending only one packet per command
- simpler design for UART asm interrupt routine knowing every packet will be one byte
*- Packets sent every 50 ms
- Tests indicated that 50ms between commands was sufficiently fast that the motion of the car was indistinguishable from constant commands
*- Packets consumed every 25ms
- Will help to ensure the buffer is not filled
*- buffer = 10 bytes (approximately half a second of backlogged packets maximum)
*: maybe sould send every 25ms and consume every 20ms so we wait a max of approximately 45ms

## Slide 17: Future Milestones
Integration of components
Fully functional interrupts
Testing of mesh network
  Self-healing
  Controlling the car
Refining protocol and code

## Slide 18: Future Projects
Video
SLAM
Multiple devices
Deployment
Notes: -deployment = vehicle dropping nodes...better term?