## Slide 1: Protocol

## Slide 2
Implemented a NAK-less reliable transport protocol
  8 bits
    Parity, ACK, Sequence, and Data bits
Parity
  1 bit detects odd number of bit errors
Ack
  Added for future implementations
Sequence
  Single alternating bit
Control Data
  5 bit OpCode

## Slide 3: RC Car

## Slide 4
Two motors
Turn-based steering
Receives commands from the controller over the network
  Uses UART to communicate with Xbee
Designed to stop if no new command received within 100ms
  Prevents car from driving away if it goes out of range

## Slide 5: Controller

## Slide 6
Intuitive control
  Uses two control sticks: Forward-Back, Left-Right
Encodes control stick input into Opcode to send to car
  Only encodes valid instructions (eg. Cannot go forward and back at the same time)
Ensures packet was received by the car before sending the next packet
  Prevents flooding of the network

## Slide 7: Future Possibilities